HY-JK05-K6 5-axis interface board manual

Thank you for choosing our products，For your use of NC products better and faster，Please read this manual

| Features：Features |
| --- |
| 1: Pulse can be equipped with an external handle with digital display, with the handle can automatically switch the computer and handle control, mutual non-interference, and automatically shielded handle control functions automatically detect the computer-controlled movement, a few significant track record computer data and handle control of mobile data 2：Computer path track record of running in the computer processing time can be record keeping, processing data offline automatically repeat the processing run. 3：Manually move the processing and record keeping, traceability records manually move the machine data, and automatically repeat the processing run manually move the path. 4：Manual data input processing path, and automatically run the input path 5: The driver XYZ-axis or Z axis of the knife can be done automatically, without the operation of complex computer software 6: Up to 3.5A stepper motor drive current, adjustable. 7: Up to 16 segments, higher accuracy, and run more smoothly. 8：Overload flow through the temperature automatic protection function, and fully protect your computer and peripherals 9: Bipolar constant-current chopper drive, low speed creeping phenomenon, noise, non-resonant region. 10: Closed optical isolation, two-stage signal processing, to fully protect your computer and equipment. 11: Rd input control, you can set the limit, stop, which is divided into the knife. 12: The maximum matching 5-axis stepper motor driver 13: The two-stage signal processing, signal transmission smooth, powerful anti-jamming 3:5 input interface to define the emergency stop, limit, points in the knife, etc. 14: relay output control interface, can be accessed by the spindle motor or the air pump, water pump, etc 15: five-axis job LED display, visual display products, working condition |
| Electrical performance (Tj = 25 ℃ ambient temperature when): |
| Input Power | 5V DC power supply or computer USB to take power |
| Work axis stepper | Received the highest 5-axis independent driving |
| Drive | Pulse + direction + enable signal. |
| Weight | About 200 grams. |
| Interface definition table: |
| Waveform and timing |
| Power output interface function |
| Interface, detailed drawing marked |

In the test machine, note the following before

1, note that using the 5V power supply

2, determine the stepper driver works (Model0)

3, to determine the drive wiring step

Operating Instructions：

1: The coordinates of display range 9999.999/-9999.999
2: automatically records the computer running coordinates and manually move the coordinates
3: Automatic switch between computer and manual control
4: computer-controlled automatically shielded manual control functions, two seconds after the return to manual function

1：ST button press the handle into the lower settings menu, set the complete press the OK button to return to the main interface

2：Replaced by B1 line, according to the four-axis handle CL button corresponding axis to 0, press the OK button to exit0

3：Four-axis real-time recording computer running coordinates and manually move the coordinates, the value of the computer running data + manually move the data

===================================================

1: all settings automatic permanent preservation until the next set of updates
2: You can set the radius, put a knife height parameters
3: The driver auto-complete the knife, without the complexity of computer software operation, convenient tool change school knife, boot knife, batch processing adequately protected on the knife and other processed products correctly

1：In order to ensure the accuracy of the knife, the knife before check put a knife height parameters and tool diameter is set correctly，

2：Need to confirm that the knife instrument wiring and limit switch wiring status is normal。

3：B2 keys and press to confirm OK to enter the automatic tool operation and automatically stop after the completion of。

====================================================

; All settings automatically saved permanently, until the next set update

; All settings automatically saved permanently, until the next set update

;

; All settings automatically saved permanently, until the next set update

; All settings automatically saved permanently, until the next set update

; All settings automatically saved permanently, until the next set update

1：ST button of the handle into the lower-level settings menu, the setup is complete press the OK button to return to the main interface

2：Downstream set shift handle B1 button，

3：Handle B2 button corresponding anti-white set at function selection

4：Handle the number keys, enter the set numeric argument

1: The coordinates of display range 0-9999.999
2: automatically records the computer running data automatically permanent preservation, to to be updated before the next recording
3: recorded 1800 segment
4: (To increase the volume can be customized plug-U disk recording the number of segments, unlimited recording)

1: Display REC state B2 key to start the computer running data record will show a record number of segments, the biggest record of 1800 segments, and then B2 button to stop.

2：Wrap press B1 keys to display the status RUN, then B2 key to start the operating records to save the computer operating data, and then B2 button to stop

3：Press ST button to enter the lower-level menu settinigs

1: The coordinates of display range 0-9999.999
2: supports both digital input manually coordinate programming and manual actually moving coordinate programming
3: recorded 1800 segment
4: (To increase the volume can be customized plug-U disk recording the number of segments, unlimited recording)

1：B2 enter the run and stop switch, switch B1 wrap

2：REC recording, press the four-axis real-time control keys to move the machine coordinates (each can only change a-axis data and then B2 key to save) save the coordinates of the real-time axis, according to the B2 key, press the CL key to manually enter the appropriate axis numeric keypad to enterthen B2 key to save the real-time axis coordinate (you can only change the axis of data B2 button to save), the recording OK and press B1 button to switch to the display RUN，

3：Press the OK button to exit back to the main interface

============================================

Please note the following before the test machine

- Test machine first to 12V voltage test machine, 42-step, please with 12-16V/DC power, 57 stepper Please choose 16-24V/DC power, 86 stepper election 24-36V/DC power

- The stepper motor power and current (model)

- Determine the wiring of the stepper motor

Second, "the definition of the pin

1 "is defined as parallel control：

| PIN14 | PIN1 | PIN2 | PIN3 | PIN16 | PIN4 | PIN17 | PIN5 | PIN6 | PIN7 | PIN8 | PIN9 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Spindle motor | enabled | X step | X dir | Y step | Y dir | Z step | Z dir | A step | A dir | B step | B dir |

2 "The limit is defined as 1 to 5

| X -Limit | Y- Limit | Z- Limit | A- Limit | 急停 |
| --- | --- | --- | --- | --- |
| PLT-P10 | PLT-P11 | PLT-P12 | PLT-P13 | PLT-P15 |

5V 1A power supply, please take more than switching power supplies, power input received indicated on the map interface

Spindle motor control is controlled via the parallel port PIN1. Spindle motor voltage must comply with the supply voltage range.

Three "MACH software to use

Figure 1

Figure 1, open the MACH3 software, then select OK now mach3MILL

Figure 2

MACH3 open the interface shown in Figure 2, the action of commonly used button above, here we configure the MACH software.

Figure 3

Figure 3, open the config menu PORT & PIN menu

Figure 4

Figure 4

Place on lap 1 setting can set the fundamental frequency, the parameters of the motor rotation speed. After 2 laps to set the place selected, the configuration pin definitions, as shown in Figure 5

Figure 5

According to the definition of the board parallel port, follow the map on the circle to indicate the definition of modification of the software settings

。

Figure 6

Then select the output signals in part, as shown in Figure 6, according to insiders of the settings, set the corresponding entry

。

Motor reference set parameters, MACH3 software manual calculation in detail and description

Figure 7

Ok all set, you can open the need to run the G code, as shown in Figure 7

Figure 8

Figure 9

Open the G code, RESET can be seen flashing red, you can use mouse click the RESET make it stop flashing, then you can press the ring 2 position CYCLESTART run.